## Slide 1
ESP GPIO | Description | Mapping to Spring Connector | Mapping to Pin Header
GPIO0 | Alive LED (active high) | Pin 6 | 
GPIO1 | MCP2515 RESET |  | Pin 7
GPIO2 | MCP2515 SPI CS |  | 
GPIO3 | MCP2515 INT_N (low active) |  | Pin 1
GPIO4 | I2C SCL (pullup) | Pin 3 | Pin 9
GPIO5 | I2C SDA (pullup) | Pin 4 | Pin 10
GPIO6 | Jumper 1: MCP2515 SPI MISO Jumper 2: CAN RX Jumper 4: MYS_MISO |  | Jumper 4: Pin 3
GPIO7 | Jumper 1: MCP2515 SPI MOSI Jumper 2: CAN TX Jumper 3: TX LED (active high) Jumper 4: MYS_MOSI |  | Jumper 4: Pin 6
GPIO8 | Relay (active high) | Pin 5 | Pin 2
GPIO10 | MCP2515 SCLK |  | Pin 5
Jumper Setting 1
SPI to CAN Controller
CAN Controller to CAN transceiver
Jumper Setting 2
ESP -> Can Transceiver
Jumper Setting 3
IO7  TX LED
Jumper Setting 4 IO7_MOSI  MYS_MOSI
IO6_MISO  MYS_MISO
ESP32 C3 Pinout

## Slide 2
Spring Clamps
MYS Pin Header
Jumper

## Slide 3
ESP GPIO | Description | Mapping to Spring Connector | Mapping to Pin Header
GPIO0 | Alive LED (active high) | Pin 6 | 
GPIO4 | Binary Sensor (low active) | Pin 3 | Pin 9
GPIO6 | Jumper 2: CAN RX |  | Jumper 4: Pin 3
GPIO7 | Jumper 2: CAN TX |  | Jumper 4: Pin 6
ESP GPIO | Description | Mapping to Spring Connector | Mapping to Pin Header
GPIO0 | Alive LED (active high) | Pin 6 | 
GPIO1 | MCP2515 RESET (optional) |  | Pin 7
GPIO2 | MCP2515 SPI CS |  | 
GPIO3 | MCP2515 INT_N (low active), optional |  | Pin 1
GPIO4 | Binary Sensor | Pin 3 (pullup) | Pin 9
GPIO6 | Jumper 1: MCP2515 SPI MISO |  | 
GPIO7 | Jumper 1: MCP2515 SPI MOSI |  | Jumper 4: Pin 6
GPIO10 | MCP2515 SCLK |  | Pin 5
ESP32 direct CAN mode
CAN via MCP2515
Jumper Setting 1
SPI to CAN Controller
CAN Controller to CAN transceiver
Jumper Setting 2
ESP -> Can Transceiver

## Slide 4
Jumper enables 120 Ohm Termination (between CAN_L
and CAN_H)
Left: USB C for UART (via CH340C) Right: USB C for Prog (via ESP CDC)
Note: PCB Labels „Prog“ and „UART“are switched :/
Jumper enables USB Power of USB prog CDC (USB Prog wrongly labelled as „UART“)
CAN Transceiver SN65HVD230
CAN Controller MCP2515
0..10V Analoge Out GP8403
Relay
USB <> UART
CH340C

## Slide 5
VCC in: 5..28V
GND
CAN L
CAN H
A0 out (0..10V)
A1 out (0..10V)
Relay
Relay
Boot (hold while pressing EN to enter Boot mode)
EN (press to restart)
3V3 LED
RX LED
TX LED
Alive LED
Spring Clamps
MYS Pin Header
Jumper
Jumper
Oopsie